## Slide 1
How the Work Fits Together
1. BUILD
27 selectable RTL configurations
2. VERIFY
RTL vs TensorFlow golden reference
3. MEASURE
Beats, bursts and cycles per knob
4. MODEL
Derive the cycle equation
5. CHECK
Validate back against RTL
6. APPLY
Score 27 combos in milliseconds
Steps 2 and 3 are different experiments. Step 2 asks "is the answer correct?" Step 3 asks "how much traffic and time did it cost?"
Steps 4 and 5 form a loop: the model is built from measured hardware, then tested back against it.
Only step 6 runs without RTL - that is the point of the analytical framework.
My contribution is step 1 (the measurable knobs) and steps 4-6 (the analytical framework).

## Slide 2
Where Every Number Comes From
Three kinds of numbers appear in this work. They are labelled everywhere, and they are not mixed.
Type | What it is | Where it appears | How strong
MEASURED (RTL) | Real Verilator runs: cycles, AXI beats, read bursts, output values | Golden check - 22 verified configurations | Hard evidence
MODEL | Closed-form predictions from my analytical framework | The chooser; the edge / cloud design-space study | Validated against the measured set
ASSUMED | Literature constants (DRAM 560 pJ/byte, MAC 0.5 pJ) | Energy figures | Cited, listed in the appendix
The large-network results (ResNet-50, BERT-Large, DLRM, VGG-16) are MODEL, never RTL. Every such chart is captioned that way.
Energy is a model quantity: RTL gives no power number. But its main input - off-chip bytes - is validated exactly, so relative energy comparisons inherit that accuracy.

## Slide 3
Why Large Networks Are Not Run in RTL
RTL simulation runs cycle by cycle - about 10,000 simulated cycles per second. A faster machine changes this by 2-5x, not by orders of magnitude.
Task | Cycles | RTL time
tiny_cnn layer_00, one configuration | 5,808 | 1.3 s
One BERT-Large layer, one configuration | ~95 M | ~2.6 hours
The same layer x 27 combinations |  | ~3 months
56 evaluation layers x 27 combinations |  | years of compute
This is not a limitation of my setup - RTL simulation does not scale to design-space exploration, by construction.
That is exactly why the analytical framework is needed. It scores 27 combinations in about 1 millisecond, against a >= 147 s lower bound for the equivalent RTL sweep on the smallest layer - roughly 100,000x faster.
And it is not needed: weights never affect cycles or traffic, so only workload dimensions matter. Bigger networks repeat the same validated computation more times.

## Slide 4
Verification - RTL Output vs TensorFlow Golden
22 / 22
configurations verified
0.0499 %
worst output error
5 %
tolerance gate
~100x
safety margin inside tolerance
Sample evidence - 2 of the 22 verified configurations
Configuration | Measured (RTL) | Golden (TF) | Error (% FS) | Result
tiny_cnn L0 - OS-ChM-Multicast | 0.709772 | 0.710062 | 0.01 % | PASS
mnist_cnn L2 - OS-ChM-Multicast | -2.005136 | -2.006291 | 0.05 % | PASS
Every configuration computes the mathematically correct answer, with roughly 100x margin inside tolerance.
Verified across all 3 stationary schemes, all 3 memory layouts, all 3 casting schemes, both memory backends (STAMP / PAGED) and three array geometries (8x8, 8x2, 8x1).
CORRECTION vs the earlier deck: this said "29 workloads". 29 is the raw file count including 7 debug probe runs (worst error 106 %). The verified set is 22 CONFIGURATIONS built from 5 layer shapes - and "configuration" is the correct word, not "workload".

## Slide 5
What Generalises - and What Does Not
WHAT GENERALISES
- The framework decides from workload GEOMETRY, not from the trained model. Weight values never affect cycles or traffic.
- All three stationary schemes, all three layouts, all three casting schemes and three array sizes are covered by measurement.
- The traffic model has NO fitted constants and matches measured beats exactly on 17 of 19 runs - including array widths it was never fitted to.
- K and output size enter as loop counts, so bigger networks repeat a validated computation more times.
HONEST LIMITS
- The RTL sweep varies ONE knob at a time. Each knob's own effect is measured; knob interactions are composed analytically, not measured.
- The compute term is interpolated for layer shapes with no measured run - it cannot change the layout or casting choice, but it can affect the stationary-scheme choice.
- Energy is a model quantity; RTL produces no power number.
- Depthwise / grouped convolution is outside the current model.
Claim made: validated for workload-based behaviour across every axis the framework selects over - not for every DNN model.

## Slide 6
Module 01 - Summary
Contribution
Made stationary scheme, memory layout and casting scheme simultaneously selectable and measurable in cycle-accurate RTL - 27 configurations from one module. No existing tool allows this.
Distilled the measured behaviour into an analytical framework that picks the best of the 27 in milliseconds.
Key findings
Finding | Evidence
Casting is the biggest lever on off-chip traffic | 1,836 -> 11,664 -> 20,736 beats (11.3x)
Layout changes REQUESTS, not data volume | same 1,836 beats; 138 vs 1,794 bursts; 1.86x faster
Runtime follows an exact law | cycles = 3 x bursts + 2 x beats + compute
Input-stationary is fastest on real hardware | 5,220 vs 5,808 cycles; the model agrees
Prediction accuracy vs measured RTL | traffic exact 17/19; cycles 0.84 % mean; 0 ranking inversions
All evidence: results/golden_check/ (measured RTL) and results/chooser/ (model). Reproducible in results/thesis_notebook/chooser_validation.ipynb.